## Slide 1: MetNet: A Neural Weather Model for Precipitation Forecasting
Presented by: Medhini Narasimhan
Casper Kaae Sønderby, Lasse Espeholt, Jonathan Heek,
Mostafa Dehghani, Avital Oliver, Tim Salimans, Shreya Agrawal,
Jason Hickey, Nal Kalchbrenner
Credits: https://vimeo.com/417618472

## Slide 2: What’s MetNet?
“a neural network that forecasts precipitation up to 8 hours into the future at the high spatial resolution of 1km2 and at the temporal resolution of 2 minutes with a latency in the order of seconds”

## Slide 3: Neural Weather Model
Probabilistic Model
Spatiotemporal Structure
Discrete Distributions

## Slide 4: What’s a Deep Neural Network?
A probabilistic model that takes an input () and predicts a probability where is a set of target labels
DNN

## Slide 5: Spatiotemporal Structure: Spatial Context
Context
Atmosphere that’s relevant
to the red patch
Predict further into the future?
More context!

## Slide 6: Spatiotemporal Structure: Temporal Context

## Slide 7: Spatiotemporal Structure
Assuming that clouds move up to 60 km/h, to predict 8 hours ahead, the model needs 60 x 8 = 480 km of spatial context. So, a 1024 km x 1024 km area is required for predictions being made on the center 64 km x 64 km patch.

## Slide 8: Discrete Distributions
Discretize output allows for multimodal prediction

## Slide 9: MetNet Data
Geostationary Operational Environmental Satellite
GOES-16 visual bands
Multi Radar Multi Sensor (MRMS) precipitation rates

## Slide 10: MetNet Architecture
Input: 4-dimensional tensor of size [t, w, h, c] that corresponds to data from a large patch
t slices sampled every 15 minutes over a 90 minutes interval prior to target lead time

## Slide 11: Conditioning on Target Lead Time
A forward pass through MetNet makes a prediction for a single lead time
By changing the target lead time given as input, one can use the same MetNet model to make forecasts for the entire range of target times that MetNet is trained on
Further into the future, the more spatial context needed, so larger the input patch!

## Slide 12: MetNet Architecture
Notes: MetNet aims at fully capturing the spatial context in the input patch. A trade-off arises between the fidelity of the representation and the memory and computation required to compute it. To maintain viable memory and computation requirements, the first part of MetNet contracts the input tensor spatially using a series of convolution and pooling layers.

## Slide 13: MetNet Architecture
Notes: The second part of MetNet encodes the input patch along the temporal dimension

## Slide 14: MetNet Architecture
Notes: To make MetNet’s receptive field cover the full global spatial context in the input patch, the third part of MetNet uses a series of eight axial self-attention blocks

## Slide 15: MetNet Output
512-way categorical distribution
Each of the 512 bins corresponds to a 0.2 mm/h interval of predicted precipitation rate starting from 0 mm/h to 102.4 mm/h
Predicted every two minutes
Learns the parameters θ governing these relations through back-propagation by minimizing the forecast error between the observed y and the predicted p(y|x)

## Slide 16: Results

## Slide 17: Results: Baselines

## Slide 18: Results: Ablations

## Slide 19: Discussion: Data
Is this an interesting/useful problem?
What other forms of input data are available? Will images taken on land help?

## Slide 20: Takeaway: Model
Why does more temporal context not help? Is the Conv LSTM causing info loss?
Data is highly unbalanced, so dist of targets is highly skewed to no rain. Not sure if they did this.
Downsampling hurts performance
OOD (training on west coast, transfer to east) also generalization over time, climate change etc. How to hard code any priors?

## Slide 21: Discussion: Results
How feasible is it to get this to work real time?
  Computational costs?
  Deployment costs?
  Use cases?
Where do you see this failing?
  Can it learn continually? Adapt as the environment changes over time? Any proofs that it can?

## Slide 22: How are weather forecasts done?
Operational weather forecasts are based on Numerical Weather Prediction (NWP) using the laws of physics to simulate the dynamics of the atmosphere.

## Slide 23: NWP vs NWM